## Slide 1: Ethernet and CSMA/CD

## Slide 2: The 4 Layer Internet Model
Network
Link
Network
Link
Transport
Application
Router
Source End-Host
Network
Link
Transport
Application
Destination End-Host
Network
Link
Router
Notes: The next layer up is, for us, the most important layer: the Network layer.
The network layer’s job is to deliver packets end-to-end across the Internet from the source to the destination.
A packet is an important basic building block in networks. A packet is the name we give to a self-contained collection of data, plus a header that describes what the data is, where it is going and where it came from. You will often see packets drawn like this: <draw a packet with header and data>
Network layer packets are called datagrams. They consist of some data and a head containing the “To” and “From” addresses – just like we put the “To:” and “From” addresses on a letter. <Draw a datagram with To/From addresses> .
The Network hands the datagram to the Link Layer below <click to wipe arrows down>, telling it to send the datagram over the first link. In other words, the Link Layer is providing a *service* to the Network Layer. Essentially, the Link Layer says: “if you give me a datagram to send, I will transmit it over one link for you”.
At the other end of the link is a router. The Link Layer of the router accepts the datagram from the link, and hands it up to the Network Layer in the router. The Network Layer on the router examines the destination address of the datagram, and is responsible for routing the datagram one hop at a time towards its eventual destination. It does this by sending to the Link Layer again, to carry it over the next link. And so on until it reaches the Network Layer at the destination. <sequence of clicks shows the steps>
Notice that the Network Layer does not need to concern itself with *how* the Link Layer sends the datagram over the link. In fact, different Link Layers work in very different ways; Ethernet and WiFi are clearly very different. This separation of concerns between the Network Layer and the Link Layer allows each to focus on its job, without worrying about how the other layer works. It also means that a single Network Layer has a common way to talk to many different Link Layers by simply handing them datagrams to send. This separation of concerns is made possibly by the modularity of each layer and a common well-defined API to the layer below.

## Slide 3
Stanford University
Cambridge University
CENIC
Internet2

## Slide 4
Stanford University
Ethernet
switches

## Slide 5
Ethernet
switch

## Slide 6: Generic Packet Switch
Lookup
Address
Data
H
Destination
Address
Forwarding
Table
Egress link
Queue
Packet
Buffer
Memory
Update
Header

## Slide 7: Generic Packet Switch
Lookup
Address
Update
Header
Forwarding
Table
Lookup
Address
Update
Header
Forwarding
Table
Lookup
Address
Update
Header
Forwarding
Table
Queue
Packet
Buffer
Memory
Queue
Packet
Buffer
Memory
Queue
Packet
Buffer
Memory
Data
H
Data
H
Data
H

## Slide 8: Ethernet Switch
Examine the header of each arriving frame.
If the Ethernet DA (aka “MAC Address”) is in the forwarding table, forward the frame to the correct output port(s).
If the Ethernet DA is not in the table, broadcast the frame to all ports (except the one through which the frame arrived).
Entries in the table are learned by examining the Ethernet SA of arriving packets.

## Slide 9: Internet Router
If the Ethernet DA of the arriving frame belongs to the router, accept the frame. Else drop it.
Examine the IP version number and length of the datagram.
Decrement the TTL, update the IP header checksum.
Check to see if TTL == 0.
If the IP DA is in the forwarding table, forward to the correct egress port(s) for the next hop.
Find the Ethernet DA for the next hop router.
Create a new Ethernet frame and send it.

## Slide 10: The Original Ethernet
Original pictures drawn by Bob Metcalfe, co-inventor of Ethernet (1972 – Xerox PARC)
Notes: I have email permission from Bob Metcalfe to use these.

## Slide 11: Ethernet Frame Format
Preamble
SFD
DA
SA
Type
Data
Pad
CRC
7
1
6
6
2
0-1500
0-46
4
Preamble: trains clock-recovery circuits
Start of Frame Delimiter: indicates start of frame
Destination Address: 48-bit globally unique address assigned by manufacturer. 1b: unicast/multicast 1b: local/global address
Type: Indicates protocol of encapsulated data (e.g. IP = 0x0800)
Pad: Zeroes used to ensure minimum frame length
Cyclic Redundancy Check: check sequence to detect bit errors.
Bytes:

## Slide 12: The origins of Ethernet

## Slide 13: Sharing a “medium”
Ethernet is (or at least was originally) an example of multiple hosts sharing a common cable (“medium”).
To share the medium, we need to decide who gets to send, and when.
There is a general class of “Medium Access Control Protocols”, or MAC Protocols.

## Slide 14: CSMA/CD Protocol
All hosts transmit & receive on one channel
Packets are of variable size.
When a host has a packet to transmit:
Carrier Sense: Check the line is quiet before transmitting.
Collision Detection: Detect collision as soon as possible. If a collision is detected, stop transmitting; wait a random time, then return to step 1.
binary exponential backoff

## Slide 15: CSMA/CD Packet size requirement
A
B
C
D
L/c
Time = 0
Time = L/c - e
Time = L/c
Time = 2L/c
First time “A” knows about collision
Therefore, “A” is guaranteed to know about the collision while it is still transmitting if:

## Slide 16: CSMA/CD Min packet size requirement
A
B
C
D
L/c
For an end host to detect a collision before it finishes transmitting a packet, we require:
where P is the size of a packet.
D
A
R

## Slide 17: CSMA/CD Min packet size requirement
A
B
C
D
Example:
R = 10Mb/s, L = 10,000m, c = 2 x 108 m/s.
L/c